# Assignment 1: Digital Circuits

You may work together with a partner. However, all source code, answers, and figures must be your own. Copying another’s work is a violation of the academic honesty policy.
Part 1 (5 pts)
Draw a rough circuit containing a Beaglebone, and LED, and a resistor designed to illuminate the LED when a GPIO pin is configured as an output and set to the HIGH state (output Vcc). What is the logic level voltage outputted by the BeagleBone?
Refer to the following product page to find the forward voltage bias of a typical surface-mount green LED. Calculate the required resistance of a series current-limiting resistor to ensure no more than 3ma is pulled from the GPIO pin.
http://www.digikey.com/product-detail/en/LG%20Q971-KN-1/475-1409-1-ND/1802597
Part 2 (5 pts)
Using the fact that the forward voltage bias of these LEDs is greater than Vcc/2, draw a second circuit with two LEDs and one resistor such that both LEDs are turned off by putting the GPIO pin into a high-impedance state and either LED can be turned on when the GPIO pin is set to HIGH or LOW.

Part 3 (5 pts)
Given the encoder wheel below. Draw the square waveforms you would expect to come out of sensors A and B through one full counterclockwise rotation of the wheel. Assume the sensor reads HIGH (Vcc) when the sensor is in a white region. Start your waveform at time zero as the wheel is currently positioned. What is the resolution of this encoder?

Part 4 (5 pts)
Imagine you are programming a microprocessor which has been tasked with counting the above encoder. It is configured to wake up on a hardware GPIO interrupt every time a signal transitions from one logic state to another, this is called edge-detection. It is also configured to execute one of the following two interrupt service routines (ISR) each time a pin sees an edge. Fill in your own pseudo-code that increments the global variable ‘position’ up or down depending on the direction of rotation. You may call the made-up functions ‘get_pin(A)’ and ‘get_pin(B)’ which will return HIGH or LOW (1 or 0) reflecting the state of the pins immediately after the interrupt.

#define HIGH 1
#define LOW 0
int position;

void pin_A_ISR(){
// Interrupt Service Routine for Pin A

}
void pin_B_ISR(){
// Interrupt Service Routine for Pin B

}
This is most easily done with if/else logic. 3 Bonus points will be awarded if each ISR contains only a single line of C code and contains no if/else statements.